## Slide 1: Waves vs Ethernet & IP VPN vs Ethernet VPN & Ethernet product comparison April 2026
Ethernet Product Management

## Slide 2: Introduction to Layers and Product positioning

## Slide 3: Product Positioning : Level 3 lies on Level 2 that lies on Level 1
IP-VPN (MPLS)
Multi-site managed networking solution
Typically lower bandwidth (100Mbps and less)
Off-net plays a key role
Customer does not need layer 3 routing skills
Ethernet / Private Ethernet
Usually two site solution (but can be multiple)
Typically 100Mbps-10Gbps
Colt’s on-net footprint is key focus
Customer DOES need layer 3 routing skills
Wave / Private Wave
Highest bandwidths (10Gbps & 100Gbps)
On-net only
Typically supports backbone networks
Layer 3
Layer 2
Layer 1
OSI Model*
* See slide 16 for OSI Stack Moel

## Slide 4: Wave and Ethernet

## Slide 5: Asia Siebel migration to global siebEl
A Series of meeting was started with Product and DIO BPA to:
Validate the mapping of Asia Siebel with EU Siebel of Ethernet services : Ethernet Line, Ethernet Hub&Spoke, Ethernet VPN and DCA
Understand Ethernet Product Variants and their volumes
Drive classification of each Product variant into the 4 categories
  1 – No difference in ASIA to EU Siebel Product features (1 to 1 mapping). Migrate directly without any product changes. Volume ~3750 items – Revenue/month : 2 073 580 €/month
  2 – Small feature difference between Source and Target Product. Migrate after Product enhancement in EU Product. Volume ~ 132 items – Revenue/month : 60 544 €/month
  3 – Products are EtherXen and are end of Sale for several years but still required for ongoing billing. Migrate as Billing Only for continuity of customer billing : no ModTech and Cease supported. (End of Life programme to be triggered at some point ) Volume ~ 213 items – Revenue/month : 87 884 €/month
  4 – Product has reached EOS and EOL. No Migration required. Volume ~ 275 items – Revenue/month : 0 €/month
Generate requirements for Product enhancement as required for Category 2
Seek agreement between ASIA and EU Product Managers that categorization is mutually agreeable.
Since the cyber incident, it was decided to migrate customer data from Asia Siebel to EU Siebel to globally align sytems

## Slide 6: Optical and Ethernet : Product positioning (1/2)

## Slide 7: Waves and Ethernet Line : product positioning (2/2)
Product | Wave / Private Wave | Ethernet Line / Private Ethernet
Platform | Wavelength Division Multiplexing (WDM) End to End dedicated bandwidth, defined and allocated per customer High bandwidths only and at line rate (no intermediate bandwidth) | Packet Network (Ethernet over MPLS) Bandwidth allocated per customer over a packet backbone underpinned by SLA Broad range of bandwidth available with intermediate steps
Topology | Point-to-Point | Point-to-Point
Usage | Enterprises requiring high performance connectivity between their DCs for real time back up of their data (no jitter, no frame loss, fixed latency). Very High bandwidth connections usually from 10G to 100G : for wholesale customers or cloud providers requiring internal backbone connections (10G to 400G) Large enterprises connecting key sites and data centres to manage their own network (often 10G/100G, sometimes 1G) Companies requiring customer-defined routing for diversity purpose. | Enterprises with 2 or more sites requiring connectivity for their Retail Buildings (10M to 100M) or between DCs (10G/40G/100G) with aggressive pricing Low to High bandwidth connections ranging from 2Mbps to 100Gbps for wholesale customers or cloud providers requiring internal high capacity backbone connections (usually 10G to 100G) Large enterprises connecting key sites with data centres (100M to 100G) Anyone needing high performance, scalable and secure bandwidth
Sweet spot | 1) Large Wholesale customers/Strategic Alliance : Microsoft, Google, Facebook, ATT, BT, Orange, … 2) Capital Market / Entreprise customers : Thomson, Porsche, Société Générale, Crédit Agricole, Hoffmann-Laroche, Morgan Stanley,… | 1) Large Enterprises/Cap. Market able to manage the Layer 3 themselves: Banque Pictet, BNP Paribas, Department of Foreign affairs, Walt Disney,… 2) Wholesale operators : ATT, Vodafone, Century Link, Tata, Deutsche Telecom,…
Performance | Deterministic performance backed with SLA : No jitter, no frame loss Fixed and low latency (fixed path) | High Standard performance backed with SLA : Small jitter and frame loss Low Latency (but may vary as routed circuit)
Delivery lead time | Rapid delivery in some DCs (10 days) Standard delivery : up to several weeks | On-Demand : near real- time delivery available in some locations Rapid delivery in some DCs (10 days) Standard delivery : up to several weeks
Price | Wave price is usually higher than Ethernet (~10%) | Ethernet price is usually lower than Wave (~10%)

## Slide 8: Supported Features Waves and Ethernet
(*1) yes for all IQNet nodes, restricted for legacy platforms (*2) Backbone is always protected including Unprotected services (*3) being developed for 2026/27
Feature | Supported features across Wave platform | Supported features across Ethernet platform
Applicable Ethernet Service rates | 1Gbit/s, 10Gbit/s, 40Gbit/s ,100Gbit/s and 400Gbit/s | 2Mbit/s to 100Gbit/s
Other customer service handoff | STM-16, STM-64, OTU-2, OTU-2e, OTU4, Fibre Channel | Not Applicable
E-line EPL Point-to-point |  | 
E-line EVPL Point-to-Multipoint |  | 
E-LAN EPLAN Multipoint-to-Multipoint |  | 
Fixed rate billing |  | 
Commit Plus Burst rate billing |  | 
Tagged & Untagged frames supported |  | 
MAC address aware |  |  (only for Ethernet VPN)
Layer 2 Protocol transparency |  |  (*1) we are transparent to the majority of L2CP
VLAN Transparency |  |  (EVPL is a VLAN aware service)
Multiple frame size support |  | 
Max Ethernet frame size | 9600 bytes (min MTU) | 9182 bytes (case by case check)
Default Customer MTU | 9600 bytes | 9100 bytes (fibre based) both EPL & EVPL Off-net : 1534 bytes (most OLO supports Jumbo frames though)
Performance reporting |  | 
Protection available |  (backbone and access) |  ( backbone and access) (*2)
Customer Interface protection (LAG) |  | 
Fixed route and latency (deterministic) |  |  (*3)
KMZ map |  |  (only for Private Ethernet)
Compliance | Interfaces compliant to IEEE 802.3 Services compliant to MEF 3.0 (E-Line) | Interfaces compliant to IEEE 802.3 Services compliant to MEF 3.0 (E-Line and E-LAN)

## Slide 9: Supported Features Waves, Ethernet, Private Ethernet
(*1) > 10Gb/s only in Key DCs (*2) yes for all IQNet nodes, restricted for legacy platforms (*3) Backbone is always protected including Unprotected services (*4) being developed for 2026/27
Feature | Supported features on Wave | Supported features on Private Ethernet | Supported features on Ethernet
Applicable Ethernet Service rates | 1Gbit/s, 10Gbit/s, 40Gbit/s, 100Gbit/s and 400Gbit/s | 1G, 2G, 3G, 4G, 5G, 6G, 10G… 100Gbit/s | 2Mb/s to 100Gb/s (*1)
Other customer service handoff | STM-16, STM-64, OTU-2, OTU-2e, OTU4, Fibre Channel | Not Applicable | Not Applicable
E-line EPL Point-to-point |  |  | 
E-line EVPL Point-to-Multipoint |  |  | 
E-LAN EPLAN Multipoint-to-Multipoint |  |  | 
Fixed rate billing |  |  | 
Commit Plus Burst rate billing |  |  | 
Tagged & Untagged frames supported |  |  | 
MAC address aware |  |  |  (only for Ethernet VPN)
Layer 2 Protocol transparency |  |  |  (*2)
VLAN Transparency |  |  |  (EVPL is a VLAN aware service)
Multiple frame size support |  |  | 
Max Ethernet frame size | 9600 bytes (min MTU) | 9182 bytes (case by case check) | 9182 bytes (case by case check)
Default Customer MTU | 9600 bytes | 9100 bytes | 9100 bytes (fibre based) both EPL & EVPL Off-net : 1534 bytes (most OLO supports Jumbo frames though)
Performance reporting |  |  | 
Protection available |  (backbone and access) |  (end to end) |  (backbone and access) (*3)
Customer Interface protection (LAG) |  |  | 
Fixed route and latency (deterministic) |  |  |  (*4)
KMZ map |  |  |  (only for Private Ethernet)
Compliance | Interfaces compliant to IEEE 802.3 Services compliant to MEF 3.0 (E-Line) | Interfaces compliant to IEEE 802.3 Services compliant to MEF 3.0 (E-Line) | Interfaces compliant to IEEE 802.3 Services compliant to MEF 3.0 (E-Line and E-LAN)

## Slide 10: Ethernet VPN and IP VPN

## Slide 11: Ethernet VPN and IP VPN : Product positioning (1/2)
Multi-site IP connectivity delivered on switched packet infrastructure
Interconnection of multiple customer sites regardless of their size
IP VPN
Layer 2 : Ethernet
Layer 3 : IP
Ethernet
VPN
Multi-site Ethernet connectivity delivered on switched packet infrastructure
Interconnecting customer HQ, DCs & branches with a layer 2 provider managed WAN

## Slide 12: Ethernet VPN and IP VPN : product positioning (2/2)
Product | Ethernet VPN | IP VPN
Platform | Packet Network (Ethernet over MPLS) Bandwidth allocated per customer over a packet backbone underpinned by SLA Broad range of bandwidth available from 2Mbps to 40Gbps | Packet Network (MPLS allows customer private network) Bandwidth allocated per customer over a packet backbone underpinned by SLA Broad range of bandwidth available from 2Mbps to 10Gbps
Topology | Multipoint-to-Multipoint (network) | Multipoint-to-Multipoint (network)
Usage | Distributed organisations with relatively small number of sites (typically < 20) requiring any-to-any connectivity for their Retail Buildings (10M to 100M), DCs (above 10G) with aggressive pricing Well suited for higher bandwidth requirements (> 1Gbps) where Ethernet connections are available Companies that want to extend their LAN across several sites or willing to manage the Layer 3 themselves (will likely deploy his own router) Some requirements for strict latency or jitter for some applications. | Enterprises with multiple sites (can be a large number) requiring a full mesh network for their branch offices and HQ across the globe Low to High bandwidth connections ranging mainly from 2Mbps to 1Gbps but with a lot of low bandwidth requirements (for e.g. DSL connections for small branch office ) Usually suitable for companies willing to have a single secure network to carry their data and unified communications (voice/video). Often requirements to provide remote access to mobile employees via their mobile or for working from home
Sweet spot | Large multinational enterprises with distributed sites in a few Colt countries: Carrefour, ING Bank, AON PLC, Allen & Overy, Kering, KPMG, Mylan, Euronext,… | Multinational companies with a large number of sites (hundreds) in many countries but with a good on-net footprint : AOK, AXA Assurances, Renault retail, Thomas Cook, UBS Group, Henner, Goldman Sachs, Lavazza, …
Performance | High Standard performance backed with SLA : Small jitter and frame loss Low Latency (but may vary as routed circuit) | High Standard performance backed with SLA : jitter and frame loss Latency (may vary as routed circuit)
Delivery lead time | Rapid delivery in some DCs (10 days) Standard delivery : up to several weeks | Rapid delivery via wireless access (14 days) Standard delivery : up to several weeks

## Slide 13: Supported Features IP VPN and Ethernet VPN
Feature | IP VPN | Ethernet VPN
Applicable Service rates | 2Mb/s to 10Gb/s | 2Mb/s to 40Gb/s
Geographies (on-net) | Western Europe, Japan | Europe, Asia, North America
Coverage | Metro, National, International | Metro, National, International
Access technology | Fiber (ULL, Colt), EFM, OLO, wDSL, 3G/4G, internet access (home office) | Fiber (ULL, Colt), EFM, OLO
Transport technology | MPLS | MPLS
Protocol | IP | Ethernet
Network Termination Equipment (NTE) |  Layer 3 (IP VPN plus)  Layer 2 (optional IP VPN) | 
Multipoint-to-Multipoint |  (a lot of sites) |  (few sites)
Fixed rate billing |  | 
VLAN Transparency |  (IP VPN is L3 network) | 
Multiple packet/frame size support |  | 
Performance reporting |  | 
Protected (backbone and Access) |  |  (*2)
Diversity |  (Resilience options) | 
Customer Interface protection (LAG) |  | 
Fixed route |  | 
Class of Service |  | 
Encryption |  |  (Bespoke)
SLA | Service availability, TTR and performance SLA | Service availability, TTR and performance SLA
(*1) yes for all IQNet nodes, restricted for legacy platforms (*2) Backbone is always protected including Unprotected services

## Slide 14: Ethernet Products

## Slide 15: Supported Features Ethernet Line, Private Ethernet, Ethernet Hub&Spoke and Ethernet VPN
Feature | Ethernet Line | Private Ethernet | Ethernet Hub&Spoke | Ethernet VPN
Applicable Service rates | 2Mb/s to 100Gb/s (*1) | 1G, 2G, 3G, … 10Gbit/s, up to 100Gbit/s | Hub : 1G, 10G, 100G Spoke : 2Mb/s to 10Gb/s | 2Mb/s to 40Gb/s
Geographies | Europe, Asia, North America | Europe, Asia (coming soon) | Europe, Asia, North America | Europe, Asia, North America
Coverage | Metro, National, International | Metro | Metro, National, International | Metro, National, International
Point-to-point |  |  |  | 
Point-to-Multipoint |  |  |  | 
Multipoint-to-Multipoint |  |  |  | 
Fixed rate billing |  |  |  | 
Commit Plus Burst rate billing |  |  |  | 
Tagged & Untagged frames supported |  |  |  | 
MAC address aware |  |  |  | 
Layer 2 Protocol transparency |  (*2) |  (*2) |  (*2) |  (*2)
VLAN Transparency |  |  |  (VLAN aware service) | 
Multiple frame size support |  |  |  | 
Max Ethernet frame size | 9182 bytes (case by case check) | 9182 bytes (case by case check) | 9182 bytes (case by case check) | 9182 bytes (case by case check)
Default Customer MTU | On-net : 9100 bytes Off-net : 1534 bytes (most OLO supports Jumbo frames) | On-net : 9100 bytes Off-net : 1534 bytes (most OLO supports Jumbo frames) | On-net : 9100 bytes Off-net : 1534 bytes (most OLO supports Jumbo frames) | On-net : 9100 bytes Off-net : 1534 bytes (most OLO supports Jumbo frames)
Performance reporting |  (only for MMSP as a standard) |  (only for MMSP at the moment) |  (only for MMSP at the moment) |  (only for MMSP at the moment)
Protected (backbone and access) |  (*3) |  (end to end) |  (*3) |  (*3)
Diversity |  |  |  | 
Customer Interface protection (LAG) |  |  |  | 
Fixed route and latency |  (*4) |  |  (*4) | 
Link Loss Forwarding |  |  |  | 
Class of Service |  (only for MMSP) | Not applicable |  (only for MMSP) | 
Encryption |  |  (bespoke) |  (bespoke) |  (bespoke)
(*1) > 10 Gb/s only in Key DCs (*2) yes for all IQNet nodes, restricted for legacy platforms (*3) Backbone is always protected including Unprotected services (*4) being developed for 2026/27

## Slide 16: Thank you

## Slide 17: The OSI (Open Systems Interconnection) model : the 7 layers model
This 7 layers conceptual model describes how computers
should “talk” to each other.
Our Network products are mainly using the first 3 layers :
IP = Layer 3 – Network
Ethernet = Layer 2 – Data Link
Wave = Layer 1 – Physical
Layer name | Description
7 – Application | Graphical user interface; primary user interface with communication system.
6 – Presentation | Supports the functionality of the application layer by providing services such as formatting and translation of data.
5- Session | Maintains the transmission path by synchronizing packets and controlling access to the medium by the Application layer.
4 – Transport | Ensures the quality of transmission and determines the best route for transmission of data using the Network layer below.
3 – Network | Finds a route for transmission of data and establishes and maintains the connection between two connected nodes.
2- Data Link | Creates, transmits, and receives packets. Controls the Physical layer.
1- Physical | Converts data into bits for transmission and converts received bits into usable data for the layers above it.
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Presentation
Session
Transport
Network
Data Link
Physical
Physical Transmission Medium
Segmented Data
L2
L3
L4
Segmented Data
L3
L4
Segmented Data
L4
Application Data
Presented Data
Procedural Data